## Slide 1: Dual-tone multi-frequency signaling (DTMF)
Realizing and Retrieving Numbers with LabVIEW

## Slide 2
Multi-frequency signaling is a group of signaling methods that use a mixture of two pure tone (pure sine wave) sounds.
The DTMF system uses a set of eight audio frequencies transmitted in pairs to represent 16 signals, represented by the ten digits, the letters A to D, and the symbols # and *
DTMF was first developed in the Bell system in the U.S. , and became known under the trademark
Touch-Tone for use in push-button telephone supplied to telephone customers, starting in 1963
DTMF signals were also used by cable television broadcasters to indicate the start and stop times of local commercial insertion points during station breaks for the benefit of cable companies.
In the UK, it is also known as MF4.
Introduction :

## Slide 3
DTMF keypad frequencies (with sound clips) |  |  |  | 
 | 1209 Hz | 1336 Hz | 1477 Hz | 1633 Hz
697 Hz | 1 | 2 | 3 | A
770 Hz | 4 | 5 | 6 | B
852 Hz | 7 | 8 | 9 | C
941 Hz | * | 0 | # | D
for example :
the key 1 produces a superimposition of tones of 697 and 1209 hertz (Hz)
Pressing a key sends a combination of the row and column frequencies.

## Slide 4
DTMF Timing (Mark and Space)
Mark : The time which a DTMF digit tone is actually producing sound, is called the "Mark" time.
Space : The silence between each one of the digits is called the "Space".
While it is a generally accepted practice to have the Space duration be the same as the Mark.
The standard for most radio decoders, as well as most telephone equipment is 40/40.

## Slide 5
LabVIEW procedure concept :
Stage I
Laptop’s microphone captures sound
Stage II
Performing FTT on cached sound
Stage III
Finding frequencies with maximum amplitude
Stage IV
Decoding top two-frequency to the specified number